## Slide 1: El-Gamal injected Elliptic Curve Cryptography based RFID Authentication for Internet of Medical Things
Presented By:
Md. Mustafizur Rahman Arman
Roll: 1707083
Supervised by:
Dr. Kazi Md. Rokibul Alam
Professor
Dept. of Computer Science and Engineering,
Khulna University of Engineering & Technology, Khulna.

## Slide 2: Outline
Introduction
Related Works
Objectives
Required Tools
Proposed Methodology
Prototype Evaluation
Conclusions
Limitations
Future Works
References

## Slide 3: Introduction
Internet of Medical things
  Mobile
  Small memory
  Low power
  Low-cost cloud computing
  Security needed for:
  Sensitive medical data
  Real-time monitoring
  Patient information management

## Slide 4: Introduction (Cont.)
Radio Frequency Identification (RFID) [3]
  Wireless communication (identify/track)
  Component:
  RFID Tag: composed of a microchip, an antenna
    and a dedicated hardware for cryptographic
    operations.
  RFID Reader: composed of a radio transmitter,
    a radio receiver, a control unit, a memory unit.
  Server: Stores all the RFID tag’s identification
    information in its database.
    Server and Reader works together as they are connected always.
Figure 1: RFID Technology

## Slide 5: Introduction (Cont.)
Figure 2: A RFID-base healthcare system
Radio Frequency Identification (RFID)
  Security Requirements for RFID Communication
  Mutual authentication
  Confidentiality
  Anonymity
  Forward security
  Availability

## Slide 6: Introduction (Cont.)
Difficulties of RFID Authentication
  Protection against unwanted access, counterfeiting, and ensuring the security and authenticity of the data transmitted.
  Maintaining anonymity, which led to issues with position tracking attack and server/reader spoofing attack.

## Slide 7: Related Works
Author/Authors | Paper | Limitations
Lijuan Zheng, Yujuan Xue, Linhao Zhang, and Rui Zhang. [8] | Mutual authentication protocol for rfid based on ecc. 2017 | Server Spoofing Attack. Position Tracking Attack. Confidentiality Problem.
Muhammad Naeem, Shehzad Ashraf Chaudhry, Khalid Mahmood, Marimuthu Karuppiah, and Saru Kumari. [7] | A scalable and secure rfid mutual authentication protocol using ecc for internet of things. 2020 | Confidentiality Problem. Tracking Attack.
Souhir Gabsi, Yassin Kortli, Vincent Beroulle, Yann Kieffer, Areej Alasiry, and Belgacem Hamdi. [6] | Novel ecc-based rfid mutual authentication protocol for emerging iot applications. 2021 | Anonymity Attack.
Table 1: Literature Overview

## Slide 8: Objectives
Authentication between RFID Tag and Server follows:
  Client-Server mutual authentication along with security goals.
  Do with Elliptic-Curve-Diffie-Hellman key agreement protocol.
  RFID Tag registration procedure confirms id stored in the Reader’s database.
  Strong Key generation procedure with El-Gamal Signature validation.
  Bit Manipulation to strengthen the security of transmitted data.
  Ensuring security of server spoofing attack, position tracking attack, anonymity.

## Slide 9: Required Tools
Figure 3: Elliptic Curve Field on X-Y axis
Elliptic Curve Cryptography (ECC) [5]
  Services:
  An alternative technique to RSA.
  Generates security between key pairs for public key encryption.
  Public-Key Cryptography based on the algebraic structure of
  elliptic curve over finite fields.
  Applicable for:
  Key agreement
  Digital signatures
  Pseudo-random generators
  ECC works on the equation of =

## Slide 10: Required Tools (Cont.)
ECC | RSA
160 | 1024
256 | 3072
384 | 7680
Table 2: Comparison of number of bits used in ECC and RSA to get same security
ECC vs. RSA [1]
  ECC is typically more appropriate for usage in resource-constrained devices and real- time applications, while RSA is more popular and well-established.

## Slide 11: Required Tools (Cont.)
El-Gamal Signature Scheme [2]
  Digital signature scheme which is based on discrete logarithms.
  Works on signing and verification a signature for authentication.
  Operations:
    Key Generation
    Signing
    Verifying Signature

## Slide 12: Required Tools (Cont.)
Bit Manipulation
  Manipulate of bits in key.
  Hard to get back to original value.
  Operations :
    Bit-wise OR
    Bit-wise AND
    Bit-wise XOR

## Slide 13: Proposed Methodology
Consists of 2 phases :
Initialization
Authentication

## Slide 14: Proposed Methodology (Cont.)
Figure 5: Initialization Phase
Initialization : 2 steps.
  Server side
    Private key s, m.
    Public key P = sQ, R = mQ.
    M = P&R.
    Send M to Tag.
  Tag side:
    Private key t.
    Pt = tQ.
    A = Pt U M.
    T = A+tA.
    Store T, Pt for further authentication.

## Slide 15: Proposed Methodology (Cont.)
Figure 6: Authentication Phase
Authentication : 4 steps.
  Tag side:
    Send T, Pt to server
  Server side:
    A’ = Pt U M
    Sg, Rg = El-Gamal_signing(T, A’)
    Send Sg,Rg to Tag.

## Slide 16: Proposed Methodology (Cont.)
Authentication : 4 steps ( Cont.)
  3) Tag side:
    B = A U (Sg & Rg)
    N = B Ꚛ T
    Send N to Server.
  4) Server side:
    B’ = A’ U (Sg&rg)
    T’ = N Ꚛ B’
    Sg’, Rg’ = El-Gamal_ signing(T’, A’)
    El-Gamal_Signature_Verification(Sg, Rg)=? El-Gamal_Signature_Verification(Sg’,Rg’)
    If it gives true, authentication successful. Else aborts.

## Slide 17: Prototype Evaluation
Figure 7: ECC key Generation
Experimental Setup
  Virtual Studio Code v1.75.0 as editor.
  Python v3.9.7 as the language for implementation.
Implementation of ECC key Generation
  secp256k1 model:
      The Curve E :
  Operations:
      EC add: 1 points from 2 other points ( C from A, B).
      EC double: 1 points from another point ( D from C).

## Slide 18: Prototype Evaluation (Cont.)
Figure 8: El-Gamal Signature Verification Flow Chart
El-Gamal Signature Verification

## Slide 19: Prototype Evaluation (Cont.)
Experimental result:
Server/Tag | Input | Output | Verification Flag
Server | s=11702, m=420838 | M=(14898407060415365318833651937377610736450856238805031296572380833665937514507, 8428029595295141819710846202898226591463894600414531680) | _
Tag | M=(14898407060415365318833651937377610736450856238805031296572380833665937514507, 8428029595295141819710846202898226591463894600414531680) |  | 
Table 3: Initialization

## Slide 20: Prototype Evaluation (Cont.)
Experimental result (Contd.):
Server/Tag | Input | Output | Verification Flag
Tag | _ | T = (31402154390291296585544318237240999221496876548904019805738349073645563392617, 22118421386738260585145428721121976033837693318874135222) Pt = (28751087112865646778086692018893182533227425746203364377961037924259350908980, 31046895123409507066835593899898841849119765084328489485) | _
Server | T = (31402154390291296585544318237240999221496876548904019805738349073645563392617, 22118421386738260585145428721121976033837693318874135222) Pt = (28751087112865646778086692018893182533227425746203364377961037924259350908980, 31046895123409507066835593899898841849119765084328489485) | S = 609171286931842029798951241489981406174479674784099060358173980863350155702515901428201120306633161989796370723222631803427801601681737526029515761343628575907 r = 495228472803037347165935762239576668030441977287935527988119465928465376294239430984752198409906680736063260771279984955777151082726644524 | _
Table 4: Authentication (step 1-2)

## Slide 21: Prototype Evaluation (Cont.)
Experimental result (Contd.):
Server/Tag | Input | Output | Verification Flag
Tag | s = 609171286931842029798951241489981406174479674784099060358173980863350155702515901428201120306633161989796370723222631803427801601681737526029515761343628575907 r = 495228472803037347165935762239576668030441977287935527988119465928465376294239430984752198409906680736063260771279984955777151082726644524 | N = 495151271918230444297773601852020715881757951045683734898095785071696353676495322808793454949939387718724804804505956277722746846071652950 | _
Server | N = 495151271918230444297773601852020715881757951045683734898095785071696353676495322808793454949939387718724804804505956277722746846071652950 | _ | True
Table 5: Authentication (step 3-4)
Successful authentication as no change occurs in the mid time of authentication.

## Slide 22: Prototype Evaluation (Cont.)
Experimental result (Contd.):
Server/Tag | Input | Output | Verification Flag
Tag | s = 609171286931842029798951241489981406174479674784099060358173980863350155702515901428201120306633161989796370723222631803427801601681737526029515761343628575907 r = 495228472803037347165935762239576668030441977287935527988119465928465376294239430984752198409906680736063260771279984955777151082726644524 | N = 495151271918230444297773601852020715881757951045683734898095785071696353676495322808793454949939387718724804804505956277722746846071652950 | _
Server | N = 495151271918230444297773601852020715881757951045683734898095785071696353676495322808793454949939387718724804804505956277722746846071652960 |  | False
Table 6: Authentication (step 3-4)
Failed authentication as change occurs in the mid time of authentication of value of N at step 3 to 4.

## Slide 23: Prototype Evaluation (Cont.)
Security Issues Comparison:
  Server Spoofing Attack:
    An attack gives an attacker the ability to pose as a legitimate system user. The attacker poses as a reader, requests information from a tag, and then receives the tag’s answer.
    70 digits long number of private key, data stored in server during registration by authorized person, unauthorized user can’t access the server easily.
  Position Tracking Attack:
  Can’t be easily accessed private keys and calculated value of Tag’s A or value of Server’s A’.
  Anonymity:
  As no position tracking attack and server spoofing attack occurs, anonymity of tag keeps secured.

## Slide 24: Conclusions
In other related works, authors proposed modular-exponential , ECC only, ECC with hashed based key generation. Where occurs some attacks and problems such as anonymity, server spoofing attack and position tracking attacks.
Compared to previous techniques, the combination of ECC, bit manipulation, and El-Gamal signature offers a stronger and more effective security solution for RFID authentication.

## Slide 25: Limitations
As 70 digits long number for private key, challenge for tag side to calculation. Needs power.
It might not consider other important aspect of RFID authentication. As there could be scenarios of supply chain management, inventory management, retail store etc.
Assumed data leaking wouldn’t occur in storage.

## Slide 26: Future Works
Real-world deployment to assess its applicability and efficacy in a real-world setting, integration with other technologies, such as biometrics or blockchain.
More tag at a time by storing data for managements.
To make sure the protocol works with a variety of systems, it can be tested using various RFID devices and readers.

## Slide 27: References
[1] Ecc vs rsa: Comparing ssl/tls algorithms. https://cheapsslsecurity.com/p/ecc-vs-rsa-comparing-ssl-tls-algorithms.
[2] El-gamal digital signature sheme. https://en.wikipedia.org/wiki/ElGamal_signature_scheme
[3] Radio-frequency identification. https://www.energyshow.com.cn/EN/Co/?CID=13&AID=3
[4] secp256k1. https://en.bitcoin.it/wiki/Secp256k1
[5] Elliptic-curve diffie–hellman, Feb 2023. https://en.wikipedia.org/wiki/Elliptic-curve_Diffie_Hellman
[6] Souhir Gabsi, Yassin Kortli, Vincent Beroulle, Yann Kieffer, Areej Alasiry, and Belgacem Hamdi. Novel ecc-based rfid mutual authentication protocol for emerging iot applications. IEEE access, 9:130895–130913, 2021.
[7] Muhammad Naeem, Shehzad Ashraf Chaudhry, Khalid Mahmood, Marimuthu Karuppiah, and Saru Kumari. A scalable and secure rfid mutual authentication protocol using ecc for internet of things. International Journal of Communication Systems, 33(13):e3906, 2020.
[8] Lijuan Zheng, Yujuan Xue, Linhao Zhang, and Rui Zhang. Mutual authentication protocol for rfid based on ecc. In 2017 IEEE International Conference on Computational Science and Engineering (CSE) and IEEE International Conference on Embedded and Ubiquitous Computing (EUC), volume 2, pages 320–323. IEEE, 2017.

## Slide 28
Thank you
Any Question?